## Slide 1: BATCH 2 WEEK 3 REPORT

## Slide 2: This weeks objectives:
Ascertain the credibility of the use of bolts in holding the nozzle and the bulkhead
Test the load cell instrumentation system
Prepare one propellant grain
Search for a material to fabricate an N2 case

## Slide 4: Open motor simulation:
Finding: peak chamber pressure 7.59 MPa

## Slide 5
Bolt surface area subjected to the shear force:
Converting the chamber pressure to force (F):
Shear stress generated on the bolts:
FORCE GENERARED = 27564 N
FINDING:
Since the shear yield strength of stainless steel is 303MPa
Achieving a safety factor=2.97

## Slide 6: Load cell testing:
Issues:
Nrf24101+ module transmits noisy data
Suggested solution:
Utilize EEPROM(AT24C256) to temporarily store data

## Slide 7: THE TEST STAND SUPPORTS
Settled on bolting as a means of connecting the supports as opposed to welding

## Slide 8: Next weeks objectives:
Melt and recast the previous cooked grains
Continue search for a 2 for the N2 case
Modify the test stand to accommodate the N2 motor
Continue testing the loadcell instrumentation system