## Slide 1: WEEK 2
Motor configuration, nozzle and casing

## Slide 3: MOTOR
The grain structure that brought desired results was the bates configuration.
The dimensions are as follows:
1. Length – 102mm x 4 cartridges
2. Diameter – 60mm
3. Core diameter – 20mm

## Slide 4: Simulation results
Average pressure – 6.57Mpa
Peak pressure – 7.52Mpa
ISP – 115.77seconds
Burn time – 1.83seconds
Motor Designation – K1095
6.

## Slide 5: Properties from simulation

## Slide 6: NOZZLE
the nozzle configurations are as follows
Throat diameter - 13.000000 mm
Exit diameter – 40.00000mm
Divergence half angle – 12 degrees
Convergence half angle – 25 degrees
Throat length – 3mm

## Slide 7: Nozzle diagrams

## Slide 8: Section view

## Slide 9: Casing
The casing of choice was Aluminum 6063 of density 2690kg/mm3 and yield strength 214Mpa
Casing external diameter – 70mm
Casing thickness taking a safety factor of 2 – 2.5mm
BURST PRESSURE – 23.75Mpa