## Slide 1: AIRFRAME TEAM WEEK 9 PROGRESS REPORT
08-06-2023

## Slide 3: secondary objectives
Fabrication and placement of fiber glass fin
Fabrication of aluminum fin
Parachute test
Primary objective
Completion of fiber glass airframe
Completion of aluminum airframe

## Slide 4: Fabrication and design of aluminum fin

## Slide 5
Aluminum Fin simulations

## Slide 6: Design process
We ran simulations on open rocket software
The final fin design was the trapezoidal section shown

## Slide 7: Fin cutting
Cut fins

## Slide 8: Fabrication and placement of fiber glass fin

## Slide 9: Fin placing process
1mm groves were made on the fiber glass frame
The airframe is placed on the alignment jig

## Slide 10
3. The fin is placed to ensure proper alignment

## Slide 11
4.Glue is then applied on the slots and the fin is placed
5. The glue is allowed to set for 30minutes

## Slide 12: Fiber glass frame with all fins placed

## Slide 13: Parachute shock cord test
Various loads were applied to the parachute to simulate the instantaneous load experienced on the shock cord during deployment
Objectives
To determine the strength of the shroud lines under loading.
To determine whether the parachute can withstand the weight of the rocket.

## Slide 14: 2.5kg
5kg

## Slide 15: observations
For the 2.5kg load no damage incurred
For 5kg load structural damage was incurred
Conclusion
The attachment of the shroud lines to the parachute was insufficient to hold the weight of the rocket. The line should be reinforced further.

## Slide 16
Solution
Revamping the shroud line attachment so that it can be stronger (currently under fabrication)

## Slide 17: Next week's objectives
Aluminum fin attachment
Structural testing of aluminum airframe
Structural testing of fiber glass airframe
Motor mount purchasing

## Slide 18: Thank you