## Slide 1
Why CFD?
Numerically solve fluids problems.
Detailed info about pressure, velocity, temperature distributions.
Approximate lift and drag forces.
Update our OpenRocket data for more accurate flight simulations.
Reduces effort and cost by avoiding physical experiments.
AIRFRAME CFD ANALYSIS
REPORT

## Slide 2
Design Workflow
OpenRocket (2D)
.ork file
SolidWorks (3D)
.STEP file
SolidWorks
.STEP file
Clean-up

## Slide 3
SolidWorks
.STEP file (Simplified)
Design Modeler
.STEP file
Export
Fluent (mesher)
.msh file
Import to
Fluent

## Slide 4
Fluent (mesher)
.msh file
Fluent (solver)
Read Mesh

## Slide 5
Preparing Geometry
CFD can’t handle complex geometry, need to simplify the geometry for CFD
Cleanup
Small faces, manufacturing features
Fillets, chamfers, rounds

## Slide 6
Enclosure
L - length of the model
Inlet - large enough to not be affected by stagnation region
Outlet - large enough to capture the wake (behind the rocket) and turbulent regions
Note that the enclosure doesn’t include the rocket - only the air around it
Rule of thumb
Actual Rocket in the enclosure

## Slide 7
Note that the enclosure doesn’t include the rocket - only the air around it.
So what do we do?
Suppress for physics!!
The rocket is a solid.
The enclosure is a fluid pool.
CFD only wants to model the fluids.
Suppress the rocket- so it doesn’t get passed to Fluent CFD (Boolean Subtract Operation)
Rocket Cavity

## Slide 8
Fluent (Meshing Software)
Setting up fluent.
Number of cores that you have
Do you have a GPU?

## Slide 9
Generated Mesh
Cross-Section area around the body tube.
20 inflation areas around the body
Body Tube C.S

## Slide 10
Around the nose cone area
Around the fin area
Skewness is less than 1.
Less than 0.8 is recommended
Number of elements in mesh 349,394

## Slide 11
Fluent Solver
Follow these steps
one by one :)
Domain tab
Physics tab
Solution tab
Results tab

## Slide 12
Performing Mesh Check-gave no errors.
Can also check quality here.
Domain Tab
PHYSICS TAB
K-Omega SST model is used
Boundary Conditions
Rocket surfaces - wall (stationary, no slip)
Inlet - velocity-inlet
Outlet - pressure-outlet
Outer wall - wall (moving at same velocity as inlet)

## Slide 13
Solutions Tab
Always initialize first. Set iterations to 500 and hit Calculate.
Residuals
Residuals should decrease by a factor of 10^3 in order to stabilize for convergent solution
Solution converged at 147 iteration

## Slide 14
Nice low Drag Coefficient
Cd=0.14
Drag Force (in the direction of airflow)
FD=136 N
Adapted from NASA rocketry website

## Slide 15
Results in CFD Post
Velocity

## Slide 16
2. Pressure Contours
Nose Cone area

## Slide 17
Fin area

## Slide 18
3. Streamlines
Cone area
Body tube area

## Slide 19
Fin area

## Slide 20
4. Vectors